## Slide 1: What Is a (Good) Process?
Professor Amit Pazgal

## Slide 2: What Is a Process?
“If you cannot describe what you are doing as a process, you do not know what you are doing.”
—W. E. Deming

## Slide 3: What Is a Process?
A process is a series of independent tasks that transforms an input into output material of higher value for the organization and its stake holders
Examples
  Toyota transforms steel, rubber, and plastic into cars.
  McDonald’s transforms meat, potatoes, and sauces into a happy meal.
  An MBA program transforms?

## Slide 4: What Is a Process? The Process View
Inputs
Outputs
Goods
and services
Labor and capital
Information
structure
Network of
activities and buffers
Flow units
(customers, data,
material, cash, etc.)
Resources
Process
management

## Slide 5: Example: Hospital Process
Outputs
Healthy people
Less pain/suffering
Improved outcomes
Death (?)
Processing
Examinations
Surgeries
Giving medications
Monitoring
Therapy
Inputs
The hospital building
Equipment
Laboratories
Medical supplies
Doctors, nurses
Other staff
Where would you put the patient?

## Slide 6: What Is a Good Process? One That Delivers Value
Delivered value of process =
benefit to process customers – total process cost
Benefit driven by customer value
Variety V
(flexibility)
Quality Q
of product or outcome
of service
Time T
Rapid, reliable delivery
New product development
Price P (Cost)

## Slide 8: Google Process
Professor Amit Pazgal

## Slide 9: Google Process Commercial

## Slide 11: Process Analysis
Flow Chart
Professor Amit Pazgal

## Slide 12: Process Analysis Flow Chart
Let’s look at the process “black box” in more detail.
Why do we need to analyze the process?
  To identify inefficient tasks
  To spot possible effectiveness improvement tasks
  To understand where value can be added
  First order of business: map the process

## Slide 13: Standard Process Mapping Symbols
Start, stop
Process step or operation
Decision point
Flow of material or work
Storage, waiting time
Delay

## Slide 14: Simplified Flow Chart for a Car Loan
Application
Review completed
Inspecting the car
Title
search
Credit
report
Start
T = 30 min.
T = 15 min.
T = 10 min.
Final
approval
T = 5 min.
Loan not approved
Approved loan

## Slide 16: Throughput Rate
Professor Amit Pazgal

## Slide 17: Process Measure: Throughput Rate
Activity
Inflow rate
Outflow rate
Throughput rate is defined as:
  The number of units flowing through an activity in a specified amount of time
For example:
  A supermarket cashier can handle 50 customers per hour
  Toyota manufactures 10 million cars per year
We usually look separately at inflow and outflow rates

## Slide 18: Process Measure: Throughput Rate II
In general, the inflow rate and the outflow rate fluctuate over time.
Define the average inflow/outflow rates as the long-run average number of jobs/units that flow into/out of the system.
In a stable environment, the average inflow rate is equal to the average outflow rate. (What if not?)
The average flow rate through the system is referred to as the throughput rate assessed as the number of jobs per unit time and is denoted by R.

## Slide 20: Throughput Time
Professor Amit Pazgal

## Slide 21: Process Measure: Throughput Time
The amount of time a job/unit spends in the process
Different units may spend different amount time in the process
The average amount of time a unit spends in the system is referred to as throughput time and is denoted by T
The throughput time for a book at Amazon.com can vary by title from a few days to several years
Book arrives
Stored
Order arrives
Picked
Packaged
Shipped
Throughput time

## Slide 22: Why Throughput Time Matters
Reduced manufacturing flow time means:
  Short delivery response time
  Reduced inventory (why?), which in turn lowers cost
  Production closer to time of sale, which increases (demand) predictability
  Fast feedback on quality problems
Reduced development flow time means:
  Quicker time to market (resulting in larger market share)
  Ease of implementing changes/improvements

## Slide 24: Inventory
Professor Amit Pazgal

## Slide 25: Process Measure: Work in Process or Inventory
Current work in process (WIP) or inventory is defined as:
  The current total number of units in the activity (system) at a given point of time
We usually refer to the average WIP or inventory and denote it by I
Example 1: What is the WIP in Disneyland?
  The physical goods waiting to be sold (food, stuffed animals, clothing items)
  The number of customers waiting, eating, resting, or playing in the park
Example 2: What is the WIP in an MBA class?

## Slide 27: Process Measures
Example
Professor Amit Pazgal

## Slide 28: Process Measurements Example: Orange Juice
Problem 3.7 From the Book
7 am to 6 pm: oranges arrive at a rate of 10,000 kilograms per hour
  Using trucks each carrying 1,000 kilograms
6,000-kilogram storage bin: when full trucks wait
Processing rate: 8,000 kilograms per hour
Although 10 trucks arrive every hour, we will draw a continuous (approximate) Inventory graph.

## Slide 29: Process Measurements Example: Orange Juice

## Slide 30: Process Measurements Example: Orange Juice
10am
8pm

## Slide 31: Process Measurements: Orange Juice—Final
The first truck that will wait arrives at 10 am.
Now, the last truck that arrives (at 6 pm) joins the longest queue and will therefore wait the longest. Thus, the last truck departs at 8pm (why?), and the maximum truck waiting time is therefore 2 hours.
Among all the 80 trucks that do wait (i.e., those arriving after 10 am), the first truck waits practically zero minutes, and the last truck waits 2 hours, culminating in an average of (0 + 2)hours/2 = 1 hour.
Overall average truck waiting time is:
  (number of trucks arriving before 10 am * 0 + number of trucks arriving after 10 am * 1 hour)/(total number of trucks) = 43.63 minutes
What changes can you make to get the trucks to wait less?

## Slide 33: Little’s Law
Professor Amit Pazgal

## Slide 34: Little’s Law
John D. C. Little was the first to prove that there is a simple relationship tying the above measurements.
Inventory (WIP) = throughput rate × throughput time
And it holds, regardless of any distributional assumption.
Obviously, R = I/T and T = I/R are just as valid.
“Units” may be measured in dollars ($).

## Slide 36: Using Little’s Law
Examples
Professor Amit Pazgal

## Slide 37: Little’s Law: Example I
Call center
Incoming calls
Completed calls
Inventory = throughput rate × throughput time
or
I = R × T
R = on average, 11 callers per minute
T = on average, a caller spends 2.5 minutes with the call center
I = average number of callers on the phone with the call center
= R × T = 11 × 2.5 = 27.5 callers

## Slide 38: Little’s Law: Example II
A busy fast-food restaurant processes on average of 1,500 customers per day (15 hours). On average, there are 75 customers in the restaurant (waiting to place the order, waiting for the order to arrive, eating, etc.).
  How long does an average customer spend at the store?
  Answer: 45 minutes
Notes: R=1500/15 hr = 100/hr I=75 so T=I/R=0.75 or 45 minutes turnover is 1/T = 4/3 customer

## Slide 39: Little’s Law: Example II—Solution
R = 1500 customers/15 hours = 100 customers/hour
I = 75 customers
T = I/R = 75/100 = ¾ of an hour = 45 minutes
What if 450 of the customers arrive for lunch (between 11:30–1:30) and even then there are 75 customers present on average?
Those customers stay in the restaurant for only
T = 75/(450/2) = 1/3 of an hour = 20 minutes
Does it make sense?
Notes: R=1500/15 hr = 100/hr I=75 so T=I/R=0.75 or 45 minutes turnover is 1/T = 4/3 customer

## Slide 40: Little’s Law: Example III—Orange Juice
Consider the orange juice example: Can we use Little’s law to determine average wait time of a truck that waits?
We consider the time period 10 am to 8 pm. Trucks arrive 10 per hour from 10 am to 6 pm, or 80 trucks overall.
7 am
Number of trucks waiting
10 am
First truck waits
8 pm
Last truck leaves
6 pm
16
R = 80/10 = 8 trucks per hour
I = 8 on average between 10 am and 8 pm (Why? 0-16-0)
T = I/R = 8/8 = 1 hour
Notes: R=1500/15 hr = 100/hr I=75 so T=I/R=0.75 or 45 minutes turnover is 1/T = 4/3 customer

## Slide 41: Little’s Law: Example IV—Clinic
Let us calculate the average waiting time in a medical clinic.
Imagine a system in which a patient can be treated in exactly 15 minutes.
Two patients arrive at minute 15, and one patient arrives at minute 45.
What is the average waiting time?

## Slide 42: Little’s Law: Example IV—Clinic (2)
Imagine the following sequence of events.
1,2
15
30
45
60
1
3
75
3
2
Waiting
Service
2

## Slide 43: Little’s Law: Example IV—Clinic (3)
In the waiting room:
Calculate average waiting time directly.
Average waiting time = (15 + 0 + 0)/3 = 5 minutes
Use Little’s law.
  Average WIP = (0 + 1 + 0 + 0)/4 = ¼ people
  Throughput = 3 people/hour
  Average waiting time = (¼)/3 = 1/12 hour = 5 minutes
Notes: Average WIP = (0 + 1 + 0 + 0) / 4 = 0.25 Average R =3/Hr so wait time = I/R=1/12 = 5 minutes

## Slide 44: Little’s Law: Example IV—Clinic (4)
For the total time spent (waiting + service):
Calculate average time spent directly
Average waiting time = (15 + 30 + 15)/3 = 20 minutes
Use Little’s law:
  Average WIP = (0 + 2 + 1 + 1)/4 = 1 people
  Throughput = 3 people/hour
  Average waiting time = 1/3 hour = 20 minutes
Notes:   Average WIP = (0 + 2 + 1 + 1) / 4 = 1 R=3 so T=1/3=20 minutes

## Slide 45: Little’s Law: Clinic—Final
If patients arrived at 15, 30, 45 minutes exactly:
  No one would wait and average stay would be 15 minutes
Randomness/variability forces resource idleness and longer waiting time.
  We will spend a lot of time on this…
Little’s law still holds!

## Slide 47: Capacity and Utilization
Professor Amit Pazgal

## Slide 48: Process Measure: Capacity
Definition: the (average) number of units, per unit of time, that can be processed
Examples
  A cashier can serve 20 customers per hour
  The capacity of a cloud server is 30,000 hits per minute
  A stove can cook 20 hamburgers per minute
    Or 0.33333 per second (Note: Units are important!)
It is a rate: units/time

## Slide 49: Process Measure: Utilization Rate
Utilization rate is a measure of efficiency.
It measures the percentage of products/services that the process is producing out of what it is designed (supposed) to do.

## Slide 50: Utilization Rate: Example
The capacity of a cashier at Starbucks is 96 customers per shift.
  Does it matter how long the shift is?
The cashier’s throughput rate is only 72 customers per shift.
  Why? Can you think of some reasons?
What is the capacity utilization? 72/96 = 0.75 = 75%

## Slide 51: Takt Time
Takt time =
  Takt time yields the rate at which customers demand product
  And the production rate to stay synchronized with demand
Example
  Demand = 150,000 cars per year
  Total available production time = 2 × 8 hours/day × 250 days/year = 4,000 hours/year
  Takt = 4,000 hours/150,000 cars = 1 hour/37.5 cars = 96 seconds/car
“The rhythm of the conductor to keep the orchestra in time”
Total time available
Customer demand
Metronome
Jeep
Notes: Key: Takt Time = 1/Throughput
Thus, LL says: Flow time = Inventory x Takt Time
@MBPF: Principles of Operations Management

## Slide 52: More About Making Cars
The total time it takes to make a car is around 15 hours (throughput time).
Due to the required takt time, Toyota, for example, has a car leave the production line every minute (throughput rate).
That would mean production line inventory of:
WIP = 15 (hours) * 60 (cars/hour) = 900 cars

## Slide 54: Bottleneck
Definition and Examples
Professor Amit Pazgal

## Slide 55: Performance Measures
What is the throughput time? How long does it take to get through the system? (time)
What is its capacity? How many units per unit time can go through each task? The process as a whole? (maximum flow rate)
What is the bottleneck? Which “production” step limits the process capacity?
Assume that a process is in place. What do we need to measure in order to understand how efficient it is?
Task 1
Task 2
Task 3

## Slide 56: What Is a Bottleneck?
A bottleneck is the process stage with the smallest throughput rate (longest production cycle).
Which task is the bottleneck?
20 units/hour
10 units/hour
15 units/hour

## Slide 57: A Different View on a Bottleneck
A bottleneck is a constraint on the process that causes revenue to be lost.
So production could be limited by an activity, but if we do not need the capacity, we say that the process is imbalanced.
In the previous example, unless more than 10 units per hour can be sold, the operations are imbalanced, but the middle station is not a true bottleneck.
20 units/hour
10 units/hour
15 units/hour

## Slide 58: Bottleneck: Example
Demand is 100 units per day. Capacities are as given.
What is the bottleneck? Capacity of the process?

## Slide 59: Bottleneck: Example
E is clearly the bottleneck limiting capacity of the entire process to 60 units.
If you look only at the subassembly, then B is the bottleneck.
Issues?

## Slide 61: Plastics Mini-Case
Professor Amit Pazgal

## Slide 62: Plastics Mini-Case
VFY (Valves for You) makes industrial valves.
For a certain product, they need nine parts that are manually assembled together.
Eight are identical plastics parts connected to a single metal part.
The metal part goes through a cutting station and a CNC machine.
The plastics parts go through molding station and then an inspection station.
All parts are then manually connected in the final assembly stage

## Slide 63: Plastics Mini-Case II
Below are the times it takes to process a part in each station (minutes) as well as the number of available machines/workers.
Can you meet a forecasted demand of 2,000 units per week if each station operates for 40 hours/week ?
Process | Time per Part | Number of Machines
Cutting | 1.6 | 1
CNC | 1.5 | 4
Plastic molding | 1.5 | 10
Inspect | 0.25 | 3
Final assembly | 3 | 2

## Slide 64: Plastics Mini-Case: Process Map
Raw material
Molding
CNC
Cutting
Start
Inspection
Final assembly
End
Off to distribution
WIP for assembly

## Slide 65: Plastics Mini-Case
Did you upload your solution?

## Slide 67: Plastics Mini-Case: Solution

## Slide 68: Plastics Mini-Case: Solution
If you have one cutoff machine running 40 hours per week, you get 40 hours × 60 minutes/hour = 2,400 minutes/week of production time available.
If it takes 1.6 minutes/part, then you can get 2,400 minutes/week/1.6 minutes/part = 1,500 parts/week from the cutting station.
CNC: Four machines can give you 4 × 2,400 = 9,600 minutes/week. Time per part is 1.5 minutes, so maximum production in a week 9,600/1.5 = 6,400.
Molding: 10 × 2,400 /1.5 = 16,000 plastic parts/week; however, each valve requires 8 plastic parts, so you can inspect at most 16,000/8 = 2000 valves/week.
Inspection: In a similar way, 3 × 2,400/0.25 = 28,800 plastic parts/week; however, each valve requires 8 plastic parts, so you can mold at most 28,800/8 = 3600. You need 8 plastic parts for each assembly, so you really only can only mold 28,800/8 = 3,600 valves.
Final assembly: 2 × 2,400 /3 = 1,600.

## Slide 69: Plastics Mini-Case: Final Map
Cutting is the bottleneck, but increasing its productivity alone will not let the firm supply 2,000 units, as the final assembly stage is also limiting.
1,500 valves week
6,400 valves week
3,600 valves week
2,000 valves week
1,600 valves week
Raw material
Molding
CNC
Cutting
Start
Inspection
Final assembly
End
Off to distribution
WIP for assembly

## Slide 71: Variability
Professor Amit Pazgal

## Slide 72: Results of (Hundreds of) Dice Experiment
Station Number | 1 | 2 | 3 | 4 | 5 | 6
Roll | 3.49 | 3.51 | 3.52 | 3.51 | 3.53 | 3.49
Transfer | 3.49 | 3.04 | 2.87 | 2.56 | 2.37 | 2.29
Average manufactured 47 (±4)
Minimum 38
Maximum 62
Chart: Experimental Results
Roll | 3.49 | 3.51 | 3.52 | 3.51 | 3.53 | 3.49
Transfer | 3.49 | 3.04 | 2.87 | 2.56 | 2.37 | 2.29

## Slide 73: So How Can We Improve the Outcome of the Experiment?
Here are some suggestions over the years:
Add workers
Increase initial inventory
Increase productivity (higher numbers on dice)
Have stations 1 and 2 help with downstream stations
Have fewer “stations”
Lower variance (variance here is completely random)

## Slide 74: More Graphs
Chart: Changing Initial Inventory
Manuf. | 44.196 | 48.1 | 51.787 | 55.264 | 58.384
WIP | 25.873 | 22.043 | 18.162 | 14.473 | 11.4
Chart: Changing Variance
| "1"-"6" | "2"-"5" | "3"-"4"
Manuf. | 48.1 | 53.775 | 59.618
WIP | 22.043 | 16.167 | 10.254

## Slide 76: Seven Key Principles of Bottleneck Analysis
The Goal
Professor Amit Pazgal

## Slide 77: Seven Key Principles of Bottleneck Analysis (the Goal)
The focus is on balancing flow, not on balancing capacity.
Maximizing output and efficiency of every resource will not maximize the throughput of the entire system.
An hour lost at a bottleneck or constrained resource is an hour lost for the whole system.
  An hour saved at a non-constrained resource does not necessarily make the whole system more productive.

## Slide 78: Seven Key Principles of Bottleneck Analysis
Inventory is needed only in front of the bottlenecks to prevent them from sitting idle, and in front of assembly and shipping points to protect customer schedules. Building inventories elsewhere should be avoided.
Work should be released into the system only as frequently as the bottlenecks need it. Bottleneck flows should be equal to the market demand. Pacing everything to the slowest resource minimizes inventory and operating expenses.

## Slide 79: Seven Key Principles of Bottleneck Analysis
Activation of non-bottleneck resources cannot increase throughput, nor promote better performance on financial measures.
Every capital investment must be viewed from the perspective of its global impact on overall throughput (T), inventory (I), and operating expense (OE).